# Circuit version 1

Illustration 1: Block schematic
Architecture
- Protection and low pass filter – This block consists of only passive elements which are providing protection against voltage spikes and noise from environment by suppressing high frequency signals. The passive elements in this stage are fairly big and robust in order to dissipate any high energy signal that may come at VIN port.
- High input impedance buffer – provides a unity gain buffering stage that has very high input impedance. Very high input impedance is needed to not compromise the signal coming from VIN port.
- Inverting gain stage – in order to support gain in range from 0.9 to 1.1 an inverting topology was used, therefore after this stage, the signal is either amplified or decreased, but it's phase is reversed.
- Inverting stage – this stage only reverts the signal phase to it's original state. No amplification is done here.
- Output buffer – this stage only buffers the signal. No amplification is done here.

Specification
No	Parameter	Test conditions	Value	Unit
1	Input impedance	1Hz - 6kHz	300k	ohm
2	Input impedance	10Hz - 500Hz	4M	ohm
3	Output impedance	50Hz	145	ohm
4	Output impedance	60Hz	115	ohm
5	Output voltage swing	Rout = 100k	+11 – 11.5	V
6	Min gain		0.909	V/V
7	Max gain		1.11	V/V
8	Low pass filter	3 dB decrease	0.72	Hz
9	High pass filter	3 dB decrease	16k	Hz

Illustration 2: Min and max gains

Illustration 3: Input impedance

Illustration 4: Output impedance

Illustration 5: 4kV burst signal shape

Illustration 6: 4kV burst tests (50 cycles)

Illustration 7: Current consumption with +/-11V input signal

Illustration 8: Signal clipping behaviour

Illustration 9: Input and output signal with gain set to 1.1
# Circuit version 2

This circuit composes of only two stages: input buffer and gain stage.

Illustration 10: Schematic of two stage circuit

Specification
No	Parameter	Test conditions	Value	Unit
1	Input impedance	1Hz - 6kHz	850k	ohm
2	Input impedance	10Hz - 500Hz	1M	ohm
3	Output impedance	50Hz	155	ohm
4	Output impedance	60Hz	125	ohm
5	Output voltage swing	Rload = 1Mohm	+11.89 ÷ –11.97	V
6	Min gain		0.5	V/V
7	Max gain		1.51	V/V
8	Low pass filter	3 dB decrease	None	Hz
9	High pass filter	3 dB decrease, Rload = 1Mohm	Below 1Hz	Hz
10	Bandwidth	3 dB decrease, Vout = 10V, Rload = 1Mohm	0.01 ÷ 500k	Hz
11	Group delay @ 50	50Hz, Gain = 1	470	ns
12	Group delay @ 60	60Hz, Gain = 1	450	ns

Illustration 11: Min and max gains

Illustration 12: Input impedance

Illustration 13: Group delay for min/max/nominal gains (green: G=0.5, red: G = 1.5, blue: G = 1.0)

Illustration 14: Group delay for nominal gain (G = 1.0)

Illustration 15: Current consumption with +/-11V input signal

Illustration 16: Signal clipping behavior

Illustration 17: Input and output signal with gain set to 1.1

# Circuit version 3

Specification
No	Parameter	Test conditions	Value	Unit
1	Input impedance	1Hz - 6kHz	870k	ohm
2	Input impedance	10Hz - 500Hz	1M	ohm
3	Output impedance	50Hz	155	ohm
4	Output impedance	60Hz	125	ohm
5	Output voltage swing	Rload = 1Mohm	+11.89 ÷ –11.97	V
6	Min gain		0.5	V/V
7	Max gain		1.51	V/V
8	Low pass filter	3 dB decrease	None	Hz
9	High pass filter	3 dB decrease, Rload = 1Mohm	Below 1Hz	Hz
10	Bandwidth	3 dB decrease, Vout = 10V, Rload = 1Mohm	0.01 ÷ over 4Meg	Hz
11	Group delay @ 50	50Hz, Gain = 1	650	ns
12	Group delay @ 60	60Hz, Gain = 1	630	ns

Illustration 18: Min and max gains
Illustration 19: Input impedance

Illustration 20: Group delay for min/max/nominal gains (green: G=0.5, red: G = 1.5, blue: G = 1.0)

Illustration 21: Group delay for nominal gain (G = 1.0)

Illustration 22: Current consumption with +/-11V input signal

Illustration 23: Signal clipping behavior

Illustration 24: Input and output signal with gain set to 1.1

Illustration 25: Two 4kV burst signals

Illustration 26: Burst signal and plotted protection resistor (Rprot) power dissipation
Average Rprot power dissipation is 6.3W.

Illustration 27: 50 burst signals and Rprot power dissipation
Average Rprot power dissipation during 1 second period is 958.87mW.